## Slide 1: PCI Express
Sean Link
David Stockhouse

## Slide 2: Overview
Sean
  Why PCI -> PCIe
  Small nuances and confusion about backwards compatibility (software vs hardware)
David
  Architecture and connection characteristics

## Slide 3: Why PCI->PCIe
PCI
  The bus shortcomings
PCIe
  Point to point. Simulated bus.

## Slide 4: Backwards Compatible?
Software
  Yes
Hardware
  No

## Slide 5: Network Architecture
Similar to OSI layers 1-4
Transaction layer
  TLP construction and management
Data link layer
  Connection management (DLLP), virtual channel control
Physical layer
  2 sublayers
  8b/10b logical encoding
  LVDS electrical connection

## Slide 6: Packet Structure
TLP – for component read/write
  Different length and contents depending on format and type
DLLP – for link control metadata

## Slide 7: Connection
Data link layer manages starting connection for new devices, through DLLPs
Each message has traffic class (TC) mapped to virtual channel (VC)

## Slide 8: Conclusion (is this necessary?)
PCIe demonstrates a movement away from parallel buses
Virtual bus replaces physical bus connections with point-to-point

## Slide 9: Questions?